## Slide 1
LocoNet
Wifi
Throttle

## Slide 7
Touch Display $20.00
Battery $ 3.00
ESP8266 $ 4.00
Filament $ 2.50
Total Material Cost $29.50

## Slide 11
Jump to your topic of interest: @ Time
Introduction Nextion Display 1:44
Making the Throttle Hardware 3:36
Throttle Main Display 5:47
Loco Control Demo 8:41
Switch Control Demo 11:08
CTC Demo 12:36
Summary 14:05
Does this all make sense? – Review 15:15

## Slide 13
Nextion
Display 3.2”
240 x 400 pixel
NodeMCU
ESP8266
Controller
(Arduino IDE)
Serial Comm 9600 Baud

## Slide 16
Connections:
1 ESP GND, Battery Minus
2 Battery Plus
10 ESP Vin
Plugging in the charger switches OFF the ESP, unplugging starts the throttle
For long time storage, keep plugged but disconnected from charger
Speaker Connector with Plug inserted
Charger Minus
Charger Plus

## Slide 26
Speed Knob
Speed Indicator
Backward Selector
Brake Button
Forward Selector
Loco Address Display
Function Buttons
Keyboard Shift
Disp Put Button
Mode Selector
Run/Idle Selector

## Slide 27
Press on Rim to set Target Speed
Current Speed Indicator
Press to change Target Direction
Press Brake Button to set 0 Speed Target
Hold for 500+ ms for immediate stop
Click to select Locomotive by Address
Click to activate / deactivate functions
Click to switch function display to F8 – F15
Click to go to Switch or CTC boards
Click to change Layout Power Status

## Slide 28: Summary

## Slide 29: Summary
Combining some cheap and readily available components allows for making a LocoNet WiFi throttle for pretty little money. I don’t know about you, but for me this generates appetite for more of the same

## Slide 30: Summary
Combining some cheap and readily available components allows for making a LocoNet WiFi throttle for pretty little money. I don’t know about you, but for me this generates appetite for more of the same
Thanks to MQTT, the throttle works like any other LocoNet throttle. You can connect as many as you want.

## Slide 31: Summary
Combining some cheap and readily available components allows for making a LocoNet WiFi throttle for pretty little money. I don’t know about you, but for me this generates appetite for more of the same
Thanks to MQTT, the throttle works like any other LocoNet throttle. You can connect as many as you want.
The Nextion display allows for making a surprisingly complex and fast user interface

## Slide 32: Summary
Combining some cheap and readily available components allows for making a LocoNet WiFi throttle for pretty little money. I don’t know about you, but for me this generates appetite for more of the same
Thanks to MQTT, the throttle works like any other LocoNet throttle. You can connect as many as you want.
The Nextion display allows for making a surprisingly complex and fast user interface
Using a 3D printer to make a case is a very flexible and effective option for makers

## Slide 34
https://www.banggood.com/3_2-Inch-Nextion-HMI-Intelligent-Smart-USART-UART-Serial-Touch-TFT-LCD-Screen-Module-p-1105286.html?rmmds=search&cur_warehouse=CN
https://www.banggood.com/6Pcs-ZOP-POWER-3_7V-750mAH-30C-1S-Lipo-Battery-JST-Plug-With-Charger-For-RC-Model-p-1329739.html?rmmds=search&cur_warehouse=CN
https://www.banggood.com/NodeMcu-Lua-WIFI-Internet-Things-Development-Board-Based-ESP8266-CP2102-Wireless-Module-p-1097112.html?rmmds=search&cur_warehouse=CN
Dispatch: http://www.digitrax.com/tsd/KB710/ut4-dispatch-a-locomotive-address/
Itead 3D Model: https://www.itead.cc/wiki/Nextion_HMI_Solution#3D_printing_bezel
Layout Intro Sequence: Beat Deola, Switzerland